# Amusement Park Physics

Directions:  Your goal is to reach 100 points in any way you wish.  You may earn up to 130 points if you want the extra credit.  Include for credit your notes from this, answers to any questions, and your calculations.  Show your work. (show the formula you are using, and then show it with the numbers in it)   Answer all questions by citing data to support your answer. (Put the numbers themselves in your answer)  Make sure that you indicate which part of this you are doing.  (i.e. Bumper cars, C)  Point values for activities are listed after the description.  Each group of 2 students needs to turn in only one report, and you both will share the score.

1. Bumper Cars

A) Linear Kinematics:  With a stopwatch and an estimated distance, measure the speed of a bumper car.  (5 pts)

B) Linear Kinematics:  Take the accelerometer aboard a bumper car.  Note what it does in 4 collisions.  What is the biggest g force you measure?  What type of collision was it? (Head on?  Sideways? rear end?...) (5 pts)

C) Momentum, Energy:  Let’s say the cars have a mass of 310 kg, add your own mass in kg to get the total mass of your car, and calculate its kinetic energy and its momentum.  (5 pts)

D) Conservation of Momentum:  When bodies collide elastically in a straight line they tend to exchange velocities.  Observe six collisions and note original velocities and final velocities of both cars.  Make nice diagrams of both cars before, and both after, using arrows for velocities.  Long arrows for greater velocities.  Is there any evidence of this exchange of velocity?  (5 pts)

2. Ferris Wheel

A) Rotational motion:  The Wheel has a radius of 8.2 m.  Time the period of rotation.  Calculate the centripetal acceleration. Convert this acceleration to "g"s (5 pts)

B) Rotational motion:  See if you can measure the difference in g force from when you are at the top of the wheel (Less g force) to when you are at the bottom of the wheel.  How does this compare with what you calculated from A)? (5 pts)

3. Looping Thunder

A) Conservation of energy:  Draw a brief but complete sketch of the ride, paying special attention to the changes in height.  The top of the first hill is 10m.  Estimate the heights of low or high spots in the track, and the initial kinetic energy given the car by the lift at the beginning..  Analyze the drawing in terms of conservation of energy, calculating what the speed should be at the different high or low spots.  Do at least 5 points. (10 pts)

B) Frames of reference:  Take the accelerometer aboard the ride and note when and what the changes of vertical g force are.  Note where extreme readings occur on your sketch.  (5 pts)

C) Frames of reference: What is the vertical accelerometer reading at the top of the loop? (5 pts)

D) Vertical Circle The loop has a radius of 3.2 m.  Calculate the minimum speed that the cars must have to go around the loop and not fall off. (ac > 9.8 m/s/s) (5 pts)

E) Vertical Circle: Calculate the cars speed from the accelerometer reading at the top, and the radius of the loop.  Remember that due to gravity, the accelerometer reading is one g less than the centripetal acceleration. (5 pts)

4. Rock-O-Plane

A) Centripetal Acceleration:  The main wheel has a radius of 7.2 m.  Time the period of rotation.  Calculate the centripetal acceleration.  Convert this acceleration to "g"s (5 pts)

B) Vertical Circle:  Ride without spinning your car.  See if you can measure the difference in g force from when you are at the top of the wheel (Less g force) to when you are at the bottom of the wheel. What is it? (5 pts)

C) Centripetal Acceleration:  Can you measure the effect with an accelerometer of rotating the cars on their own axis?  What is it? (5 pts)

5. Round Up

A) Centripetal Acceleration:  Time the rotational period. The radius is 3.4 m.  Use these to calculate the centripetal acceleration.  Convert this acceleration to "g"s (5 pts)

B) Vertical Circle:  Use the accelerometer aboard the ride to measure the g force at the top and the bottom.  How does this compare to the calculated value?  (Remember that you should measure one less at the top, and one more than the calculated “g” force) (5 pts)

6. Scrambler

A) Frames of reference:  Take an accelerometer aboard the ride and point it to the outside of the car.  Watch it as the ride runs, and note when the reading is the highest.  When is the reading the highest?  How and why does this correlate with the position of the ride?  (5 pts)

7. Spider

A) Frames of reference:  Take an accelerometer aboard the ride and point it to the outside of the car.  Watch it as the ride runs, and note when the reading is the highest.  When is the reading the highest?  How and why does this correlate with the position of the ride?  (5 pts)

B) General:  How does the spider achieve its alluring up and down motion?  Draw a brief but complete picture of the actual mechanism responsible and explain it.  (5 pts)

8. Big Pink Slide

A) Energy  Let’s say the Big Pink is 4.6 m high.  Estimate your mass in Kilograms.  (Divide your weight in pounds by 2.2 to get this).  Calculate your potential energy in Joules. (5 pts)

B) Conservation of energy  Calculate what your velocity should be at the bottom of the Big Pink.  (Set PE = KE)  Do you think you are going that fast at the bottom?  Where else (besides into KE) could the energy have gone?  (10 pts)

C) Power Time how long it takes you to climb the Big Pink stairs.  Calculate your power output.  Don't run.  (5 pts)

9  Tilt-A-Whirl

A) Frames of reference:  Take an accelerometer aboard the ride and point it to the outside of the car.  Watch it as the ride runs, and note when the reading is the highest.  When is the reading the highest?  How and why does this correlate with the position of the ride?  (5 pts)

10. Go-Karts

A) Centripetal acceleration  Estimate the speed of the Go-Karts.  (divide mph by 2.238 to get m/s)  Estimate the radius of one of the corners.  What is the centripetal acceleration of the Kart around the corner?  (5 pts)

B) Friction  Guess the mass of one of the Karts and rider (or not).  Set the centripetal force equal to the force of friction.  Solve for the coefficient of friction. (5 pts)

C) Friction What kind of friction do you want when cornering?  (static, kinetic)  What will happen if you start to slide around a corner?  (5 pts)

11. Train

A) Linear Kinematics: Use a measured distance and time to calculate the top velocity of the train in m/s.  Time how long it takes the train to reach top speed from rest.  Calculate its acceleration.  (10 pts)

B) Energy:  Estimate the mass of the locomotive, the train and its riders. (in kg)  (Pick a representative car, count the people and multiply by 70 kg or so, and guess for the car.  add 'em all up)  Use your calculated velocity from A) to calculate the maximum kinetic energy of the train. (5 pts)

C) Dynamics:  Using Newton's second law, calculate the force the tracks must exert on the train to accelerate it.  (Use the whole mass of the train for this!)  Also calculate what the coefficient of friction has to be in order for the locomotive to do this.  (The normal force would be due to the mass of only the locomotive.)  (10 pts)

D) Power: Using the kinetic energy as work and the time from A), calculate the power output of the train while it is speeding up from rest. (5 pts)

12.Screaming Eagle

A) Pendulums: Use the formula for the period of a pendulum to calculate the length of the ride from the bottom to the hinge point.  (T = 2(L/g)1/2)  (Time the period - it is the time for one complete cycle.  From when it is all the way to one side to when it is there again, not the time separating bottom dead centers which is 1/2 a period, then use the formula to calculate the length.) (5 pts)

B)Trigonometry: Use the length and an estimated angle above bottom dead center to calculate how high the bottom of the ride gets off the ground. (it is L-Lcos(angle)) (5 pts)

C)Conservation of Energy: Calculate the speed of the ride at the bottom using how high it gets and conservation of energy. (5 pts)

D) Centripetal Acceleration: Calculate the centripetal acceleration at the bottom of the ride due to the pendulum motion.  Convert this acceleration to "g"s  (5 pts)

E) Vertical Circle: Ride the ride with an accelerometer and measure the vertical g force at the bottom.  Is it one more “g” than what you calculated in part D)? (5 pts)

13 Carousel.

A) Centripetal Acceleration:  Suppose the radius of the ride is 5.2 m, and time the period of rotation.  Calculate the tangential velocity and the centripetal acceleration.  Convert the centripetal acceleration to "g"s.  Can you measure this with your accelerometer?  (5 pts)

B) Coriolis Effect:  Ride with one of you on the inside, and the other on the outside.  Toss a paper wad back and forth.  Does it appear to curve?  Draw a picture of the ride from above, and note the direction of rotation, the direction you threw the paper wad, and the way it curves.  Show the curve throwing in, and throwing out.  (don't throw up) (10 pts)

14 Rock and Roll (aka The Erupter aka The Matterhorn)

A) Centripetal Acceleration:  The radius is about 5.4 m.  Time the period of motion.  Calculate the tangential velocity and centripetal acceleration. Convert this acceleration to "g"s (5 pts)

B) Centripetal Acceleration:  Take an accelerometer aboard and measure the centripetal acceleration.  Compare it to the calculated value.  (5 pts)

C) Frames of reference:  The cars in the Rock and Roll are on pivots.  This means that they always hang in the direction of "down" in the accelerated frame of reference of the car.  How and why does this direction change with respect to the earth frame as the cars go around the track?  (5 pts)

15 The Frog Hopper

A) “g” Force  Ride and measure the vertical “g” force.  What is the smallest you measure, what is the biggest? (5 pts)

B) “g” Force  What is the actual upward and downward acceleration the ride undergoes?  (hint – subtract 1 “g” from the readings in A) (5 pts)