PreQuiz 11.1

Simple Harmonic Motion

Name

Favorite YouTube Video

1. An SHO has a speed of 2.15 m/s when it is 0.23 m from equilibrium.  What is its period if its amplitude is 0.47 m? (1.2 s)

(1.2 s)

2. An SHO has an equation of position (in m) of x = 7.2sin(5.1t)  What is its maximum velocity?

(37 m/s)

3.  Write the equation of position for an SHO that has an equation of velocity of v = 24cos(6.0t).

(x = 4.0sin(6.0t))

4.  An SHO has a mass of 3.61 kg, a period of 4.17 s, and a total energy of 15.7 J.  What is its amplitude?

(1.96 m)

5.  An SHO has a mass of 1.83 kg, a frequency of 10.0 Hz, and amplitude of 0.18 m.  What is its potential energy when it is 0.13 m from equilibrium?

(61 J)