IB Physics

Pre-Quiz 20.2

Name

Favorite Composer/Songwriter

Show your work, circle your answers, and use sig figs to receive full credit.

1. 18.2 A of current flow east along a wire in a magnetic field of 0.0150 T that is 17.0o east of North.  What force acts on the wire if it is 113 m long?  (Magnitude and direction) (29.5 N Up)

2. A 4.2 Amp current flows North in a wire that is 12.1 cm long.  What is the magnetic field (Assume it is perpendicular) if the wire experiences a vertically upward force of 12.15 N?  (Magnitude and direction) (24 T West)

3. An electron travels at 3.5 x 104 m/s to the North, and experiences a force of 2.1 x 10-14 N vertically downward.  What is the magnitude and direction of the magnetic field exerting this force? (3.7 T W)

4. A proton is going 1.71 x 105 m/s in the plane of the page in a 2.30 T magnetic field out of this page. What is the radius of its path?  Which direction does it circle, ACW or CW?  (7.76x10-4 m, CW)

5. What electric field in what direction would make the particle go straight up the page in the previous problem? (3.93x105 N/C, Left)

# Text boxes

N

W      E

S