## Stars Part I – Brightness and Distance

#### Wien’s Law - Temperature

λmax = 2.90 x 10-3 m/K

T

λmax = Peak black body wavelength

T = The star’s surface temperature in Kelvins

# Total Power Ouput

Luminosity L = σAT4

Luminosity L = The star’s power output in Watts

σ = Stefan Boltzmann constant

A = The star’s surface area = 4πr2

T = The star’s surface temperature in Kelvins

## Apparent Brightness

Apparent Brightness b = L

4πd2

b =  The apparent brightness in W/m2

L = The star’s Luminosity (in Watts)

d = The distance to the star

# Apparent Magnitude

Apparent Magnitude m = 2.5log10 (2.52 x 10-8W/m2/b)

b =  The apparent brightness in W/m2

m = The star’s Apparent Magnitude

## Absolute Magnitude

Absolute Magnitude M = m - 5 log10(d/10)

M = The Absolute Magnitude

d = The distance to the star in parsecs

m = The star’s Apparent Magnitude

Hot stars are:

Big, Bright, Brief and Blue

Cool stars are:

Diminuitive, Dim, and Durable and um… reD

Spectral Types

O – 30,000 - 60,000 K, ionized H, weak H lines, spectral lines are

spread out.  O types are rare and gigantic.

B – 10,000 - 30,000K, H lines are stronger, lines are less spread out

(Rigel, Spica are type B stars)

A – 7,500   - 10,000K, strong H lines, Mg, Ca lines appear (H and K) (Sirius, Deneb and Vega are A type stars)

F – 6,000   - 7,500K, weaker H lines than in type A, strong Ca lines

(Canopus (S.H.) and Polaris are type F)

G – 5,000   - 6,000K,  yellow stars like the sun.  Strongest H and K

lines of Ca appear in this star.

K – 3,500    - 5,000K, spectrum has many lines from neutral metals.

Reddish stars (Arcturus and Aldebaran are type K stars)

M - 3,500 or less, molecular spectra appear.  Titanium oxide lines

appear.  Red stars (Betelgeuse is a prominent type M)

Suffixes 0 (hottest) - 9 (coolest) so O0, O1…O9, then B0, B1…