## Slide 1
Pressure
  Contents:
    How to calculate
    Whiteboards
    Gauge pressure
    Whiteboards

## Slide 2
Pressure is in Force per unit area
  F = Force in N
  A = Area in m2
  P = pressure in N/m2 (Pascals - Pa)
Demo - 1 m2 – Show what a Pa is (atm in each Pa, lb/in2)
In a fluid– Same in all directions, perp to walls.

## Slide 3
Pressure is in Force per unit area
  F = Force in N
  A = Area in m2
  P = pressure in N/m2 (Pascals - Pa)
Example - A 2.4 kg box measures 15 cm by 25 cm on the base. What is the pressure under the box?
(630 Pa – snowshoes vs. spike heels)
F = mg
A = LxW

## Slide 4
Pressure
1 | 2 | 3

## Slide 5
A = (.20 m)(.32 m) = .064 m2
P = F/A = (42 N)/(.064 m2)
660 Pa
What is the pressure of 42 N on a 20. cm x 32 cm plate?

## Slide 6
A = LxW
A = (.780 m)(1.82 m) = 1.4196 m2
P = F/A, F = PA = (3200 Pa)(1.4196 m2)
4540 N
What force does 3.200 kPa exert on a 78.0 cm x 182 cm pane of glass?

## Slide 7
Find area
A = r2 for a circle
Diameter = 2r
P = F/A, A = F/P = (31360 N)/(1.38 x 106 Pa)
A = .022725 m2
A = r2
r = .08505 m
d = 2r
0.170 m
A hydraulic jack lifts a 31,360 N car using a pressure of 1.38 MPa (M = x 106) What is the diameter of the cylinder?

## Slide 8
Converting units of pressure
1 atm = 1.013x105 Pa = 101.3 kPa = 760. torr = 14.7 PSI
(1 bar = 1x105 Pa, so 1 atm = 1.013 bar)
Convert 2.10 atm to Pa: (2.13x105 Pa)
Convert 345 torr to Pa: (4.60x104 Pa)
Convert 2.45x104 Pa to PSI: (3.56 PSI)

## Slide 9
Conversions
1 | 2 | 3

## Slide 10
=(32/14.7)*101.3 = 220 kPa
220 kPa
Convert 32 psi to kPa
1 atm = 1.013x105 Pa = 101.3 kPa = 760. torr = 14.7 PSI

## Slide 11
=(890/760)*1.013E5 = 1.2E5 Pa
1.2x105 Pa
Convert 890 Torr (mm Hg) to Pa
1 atm = 1.013x105 Pa = 101.3 kPa = 760. torr = 14.7 PSI

## Slide 12
=(2000/14.7)*1 = 136 atm ≈ 100 atm
136 atm ≈ 100 atm
Convert 2000 psi to atm:
1 atm = 1.013x105 Pa = 101.3 kPa = 760. torr = 14.7 PSI

## Slide 13
Gauge pressure
Most pressure gauges compare to Atmospheric
Gauge pressure is how much more a pressure is
than atmospheric
(i.e. this room is at 0 Gauge - Absolute P is 1 atm more)
P = Pgauge + PAtm
  P = Absolute (actual) pressure
  Pgauge = Gauge pressure
  PAtm = Atmospheric pressure
Demo - Magdeberg Hemispheres
Boiling can
How straws work

## Slide 14
Gauge pressure
P = Pgauge + PAtm
  P = Absolute (actual) pressure
  Pgauge = Gauge pressure
  PAtm = Atmospheric pressure
Example 1 – If your tyre pressure gauge reads 220 kPa, what is the actual pressure in the tyre in kPa and Pa?
(320 kPa, 3.2E5Pa)
1 atm = 1.013x105 Pa = 101.3 kPa = 760. torr = 14.7 PSI

## Slide 15
Gauge pressure
P = Pgauge + PAtm
  P = Absolute (actual) pressure
  Pgauge = Gauge pressure
  PAtm = Atmospheric pressure
Example 2 – What is the gauge pressure if you have an actual pressure of 1072 Torr? (312 Torr)
1 atm = 1.013x105 Pa = 101.3 kPa = 760. torr = 14.7 PSI

## Slide 16
Gauge pressure

## Slide 17
Gauge Pressure
1-4

## Slide 18
P = Pgauge + 1 atm
P = 35 psi + 14.7 psi = 49.7 psi
1.013E5*49.7/14.7 = 3.42E5 Pa
49.7 psi, 3.42E5 Pa
What is the absolute pressure if you read 35 psi gauge? Answer in psi and Pascals
1 atm = 1.013 x 105 Pa = 101.3 kPa = 760 Torr = 14.7 psi

## Slide 19
P = Pgauge + 1 atm
812 = Pgauge + 760 Torr
Pgauge = 52 Torr
52 Torr
If you have an absolute pressure of 812 Torr, what is the gauge pressure? Answer in Torr
1 atm = 1.013 x 105 Pa = 101.3 kPa = 760 Torr = 14.7 psi

## Slide 20
P = Pgauge + 1 atm
P = 2.17 x 105 Pa + 1.013 x 105 Pa
3.18 x 105 Pa
What is the absolute pressure if the gauge pressure is 2.17 x 105 Pa. Answer in Pa.
1 atm = 1.013 x 105 Pa = 101.3 kPa = 760 Torr = 14.7 psi

## Slide 21
P = Pgauge + 1 atm
42.0 kPa = pgauge + 101.3 kPa
-59.3 kPa
If you have an absolute pressure of 42.0 kPa, what is the gauge pressure in kPa?
1 atm = 1.013 x 105 Pa = 101.3 kPa = 760 Torr = 14.7 psi