## Slide 1
Pascal’s Principle
  Contents:
    How to calculate
    Whiteboards

## Slide 2
A confined fluid transmits external pressure:
Demo - hydraulic jack

## Slide 3
Example – A hydraulic jack has an input piston with a diameter of 8.20 mm, and an output piston diameter of 95.0 mm. What force in Newtons do you need to apply to lift a ton? (8900 N) What is the pressure in Pa? How far must you move the input cylinder to raise the car 10.0 cm?
(66.3 N, 1.25E6 Pa, 1340 cm)

## Slide 4
Pascal’s Principle
1 | 2 | 3

## Slide 5
465 N
A car has a master cylinder bore size of 2.50 cm, and a caliper bore of 4.40 cm. What force does the caliper exert if you press on the master cylinder with a force of 150 N?

## Slide 6
0.0042 m or 0.42 cm
A hydraulic jack has an output cylinder with a 5.2 cm bore, and needs to lift a 53,400 N weight with an input force of 356 N. What is the diameter of the input cylinder needed?