## Slide 1
Power
  Definition
  Whiteboards

## Slide 2
Power
  power = work
    time
Derive all eqn using:
V = W/q
I = q/t
R = V/I
P = IV = I2R = V2
  R
  P: Power in W
  I: Current in Amps
  V: Voltage in Volts
  R: Resistance in Ohms
Example 1: If a car stereo uses 850 Watts of power, how many Amps does it use at 12 V?
P = IV, I = P/V = (850 W)/(12 V) = 70.8333 = 71 A (alternators supply about 50 A)
Example 2: If you have 128 mA of current running through a 560 ohm resistor, what power will it dissipate, and what is the voltage across it?
P = I2R. P = (.128 A)2(560 ) = 9.175 W = 9.2 W, V = IR = 71.68 = 72V
Demo: power supply and heating element, motor and ammeter

## Slide 3
Whiteboards
1 | 2 | 3 | 4 | 5 | 6

## Slide 4
A heating element draws 2.07 A from a 12.0 volt source. What is the power it consumes?
24.8 W
Given:
P = IV = I2R = V2
  R
  P = ??
  V = 12.0 V
  I = 2.07 A
Use P = IV
P = 24.84 = 24.8 W

## Slide 5
What is the current flowing in a 75 W light bulb connected to 120 V?
.625 A
Given:
P = IV = I2R = V2
  R
  P = 75 W
  V = 120. V
  I = ??
Use P = IV
I = .625 A

## Slide 6
What is the power used by a 0.135 ohm heating element connected to a 24.0 V source?
4270 W
Given:
P = IV = I2R = V2
  R
  P = ??
  R = .135 
  V = 24.0 V
Use P = V2/R
P = 4266.66 = 4270 W

## Slide 7
A 345 mW light bulb draws 12.8 mA of current. What is its resistance?
2110 
Given:
P = IV = I2R = V2
  R
  P = .345 W
  R = ??
  I = .0128 A
Use P = I2R
R = 2105.73 = 2110 ohms

## Slide 8
A 0.25 Watt 1000. ohm resistor can be connected to what maximum voltage?
16 V
Given:
P = IV = I2R = V2
  R
  P = .25 W
  R = 1000. 
  V = ??
Use P = V2/R
V = 15.81139 = 16 V

## Slide 9
What maximum current can flow through a 50.0 ohm resistor that is rated at 10.0 Watts?
447 mA
Given:
P = IV = I2R = V2
  R
  P = 10.0 W
  R = 50.0 
  I = ??
Use P = I2R
I = .447214 = 447 mA