## Slide 1
Resistivity
  Definition
  Whiteboards

## Slide 2
What determines the resistance of a piece of wire?

## Slide 3
Resistivity: consider a piece of wire:
  L - Length of the wire in m
  A - Cross sectional area of the wire (πr2 ?)
  R - Resistance of the wire in Ohms
Demo: Different wires
L
A
Some values of ρ in Ωm at 20oC (From table 18-1 on p 535)
Silver 1.59E-8
Copper 1.68E-8
Gold 2.44E-8
Aluminium 2.65E-8
Tungsten 5.6 E-8
Iron 9.71E-8
Platinum 10.6E-8
Nichrome 100E-8
(alloy of Ni, Fe, Cr)
R = ρL
  A
ρ - Resistivity in Ωm

## Slide 4
Some values of ρ in Ωm at 20oC (From table 18-1 on p 535)
Iron 9.71E-8
R = ρL
  A
Ex #1: A steel wire is 2.7 m long, and has a resistance of 7.3 ohms. What is its diameter? (0.21 mm)

## Slide 5
Whiteboards
1 | 2 | 3

## Slide 6
A copper wire is 1610 m long (1 mile) and has a cross sectional area of 4.5 x 10-6 m2. What is its resistance? (This wire is about 2.4 mm in dia)
6.0 Ω
Silver 1.59E-8
Copper 1.68E-8
Gold 2.44E-8

## Slide 7
An Aluminium wire is 3.2 mm in diameter, and has a resistance of 142 ohms. What length is it?
43,000 m
Gold 2.44E-8
Aluminium 2.65E-8
Tungsten 5.6 E-8

## Slide 8
A piece of wire has a diameter of 0.42 mm, and a length of 53 cm. What is its resistivity if it has a resistance of 4.9 ohms? (what kind of wire is it?)
130x10-8 Ωm
Iron 9.71E-8
Platinum 10.6E-8
Nichrome 100E-8