## Slide 1
Ohm’s Law
  Definition
  Whiteboards
  An Elaborate Analogy

## Slide 2
Ohm’s Law
  V = Voltage (like pressure)
  I = Current (like flow rate)
+
-
A
R
    R = Resistance in ohms ()
    V = Voltage in Volts (V) (pressure)
    I = Current in Amps (A) (flowrate)
V

## Slide 3
Ohm’s Law - The way I think of it
  V = Voltage (like pressure)
  I = Current (like flowrate)
  R = Resistance to flow
+
-
A
R
  I = V
  R
    R = Resistance in ohms ()
    V = Voltage in Volts (V) (pressure)
    I = Current in Amps (A) (flowrate)
V

## Slide 4
Ohm’s Law
+
-
A
R
I = V
R
  R = Resistance in ohms ()
  V = Voltage in Volts (V) (pressure)
  I = Current in Amps (A) (flowrate)
V
Black 0
Brown 1
Red 2
Orange 3
Yellow 4
Green 5
Blue 6
Violet 7
Gray 8
White 9
Gold 5%
Silver 10%
No color 20%

## Slide 5
Ohm’s Law
+
-
A
R= ??
    R = Resistance in ohms ()
    V = Voltage in Volts (V) (pressure)
    I = Current in Amps (A) (flowrate)
12.0 V
120. mA
Example 1: What is the resistance in the circuit above? (100 Ω)
Example 2: If there is a 220  resistor in the circuit above, what is the current? (0.055 A)

## Slide 6
Whiteboards
1 | 2 | 3 | 4 | 5 | 6

## Slide 7
What is the resistance of a light bulb if it draws 250 mA of current from a 6.15 V battery? (1000 mA = 1 A)
24.6 

## Slide 8
What current will flow if you plug a paperclip with a resistance of 0.065  into a 12 V source?
180 A

## Slide 9
What voltage do you need to push 1.5 Amps of current through a 210 ohm resistor?
315 V

## Slide 10
What current flows through an 8.1 ohm speaker when there is a voltage of 3.45 V?
0.43 A

## Slide 11
An unknown resistor draws 0.0128 Amps of current from a 23.9 V source. What is the resistance?
1870 

## Slide 12
A 1200 ohm resistor is hooked up to an unknown voltage source, and it draws 87.5 mA of current. What is the voltage?
105 V

## Slide 13
A 670 ohm resistor is connected to a 1.5 V battery. What time will it take for 3.0 C of charge to flow from the battery?
1340 s

## Slide 14
A 3.0 V battery with a capacity of 350 mAh (350 milli amp hours) is drained in 4 hours and 27 minutes. What is the resistance of the circuit that it is attached to?
38 

## Slide 15
Symbols

## Slide 16
Symbols

## Slide 18
An analogy
Water in pipes: Electrons in wires:
Flow rate (GPM) Current (Amps = C/s)
Pressure Voltage
Constriction Resistance
Constant P Pump Batteries/Cells
+
-
A3
R1
R2
Current convention
Restriction
Wires are superconductors