## Slide 1
Power
  Definition
  Whiteboards

## Slide 2
Power
  power = work
    time
Derive all eqn using:
P = IV = I2R = V2
  R
  P: Power in W
  I: Current in Amps
  V: Voltage in Volts
  R: Resistance in Ohms
I = q/t

## Slide 3
Example 1: If a car stereo uses 850 Watts of power, how many Amps does it use at 12 V? (71 A)
Example 2: If you have 128 mA of current running through a 560 ohm resistor, what power will it dissipate, and what is the voltage across it? (9.2 W, 72 V)

## Slide 4
Whiteboards
1 | 2 | 3 | 4 | 5 | 6

## Slide 5
A heating element draws 2.07 A from a 12.0 volt source. What is the power it consumes?
24.8 W

## Slide 6
What is the current flowing in a 75 W light bulb connected to 120 V?
0.625 A

## Slide 7
What is the power used by a 0.135 ohm heating element connected to a 24.0 V source?
4270 W

## Slide 8
A 345 mW light bulb draws 12.8 mA of current. What is its resistance?
2110 

## Slide 9
A 0.25 Watt 1000. ohm resistor can be connected to what maximum voltage?
16 V

## Slide 10
What maximum current can flow through a 50.0 ohm resistor that is rated at 10.0 Watts?
447 mA