## Slide 1
1. A loop or wire with a radius of 0.78 m is in the plane of this page, and is rotated so that the loop forms a 23.0o angle with the page. If there is a 3.72 T magnetic field into the page, and the rotation takes .015 s, what is the average EMF generated? Which way does it flow? (38 V, CW)

## Slide 2
2. The wire below is 2.28 m long (really!) and is traveling through a 6.71 T magnetic field out of the page. What is its speed if there exists a potential of 41.6 V from one end to the other? Label the positive end of the wire. (2.72 m/s bottom is +)

## Slide 3
3. A transformer has 350 primary windings, and 1600 secondary windings. What is the voltage in the primary if there is a voltage of 512 V (AC) in the secondary? (112 V)

## Slide 4
4. You want to step 120 VAC down to 9.6 VAC with a transformer. What should be the number of secondary windings if you have 1800 primary windings? (144 windings)

## Slide 5
5. A transformer steps 240 VAC down to 1.5 VAC. What current flows in the secondary if the primary side has 2.6 A flowing through it? (416 A)