# Uncertainty –

# Any measurement or value in Physics will have an uncertainty.  Here’s how to estimate that uncertainty:

- Measuring with a ruler: The uncertainty is ± half the smallest division on the ruler.  If you measure something that is 12.4 cm long with a ruler that has mm divisions, then your uncertainty is ± .5 mm or ± .05 cm so you would say 12.4 ± .05 cm

- Using a digital readout: The uncertainty is ± the last digit.  If you have an ammeter that reads 1.56 Amps, it would be 1.56 ± .01 Amps.

- Multiple trials of something with random error: You could say that it is the average, ± range/2.  If you did 3 trials for the rocket lab, and a rocket stayed up in the air for 5.23, 5.25, 5.12, and 5.36 seconds, you could say that it is 5.24 (the average) ± .12 (the range/2, i.e. (5.36-5.12)/2).

# Propagating Uncertainty:  When you do calculations with numbers that have uncertainty, the answer has uncertainty as well.  There are different rules for addition/subtraction and for multiplication/division, and I will show you them in class.

# Directions: The answers are on the side. (Uncertainties should be rounded to 1 or 2 sig figs, and the number of decimal places in the answer should not exceed the limit of the uncertainty)

Adding or subtracting – the uncertainty of a sum or difference is the sum of the uncertainties

| 25.2 ± .7 | 13.1 ± .2 | 23.12 ± .01 | 24 ± 2 | 21.3 ± .5 |
| --- | --- | --- | --- | --- |
| 6.87 ± .03 | + 12.1 ± .5 | - 16.25 ± .02 | + 127 ± 5 | - 21.1 ± .1 |
| 151 ± 7 |  |  |  |  |
| .2 ± .6 |  |  |  |  |

Multiplying and/or dividing – if y = ab/c, then (y/y = (a/a + (b/b + (c/c (( reads uncertainty of)  Round uncty to two sig figs.

| 31.6 ± 3.8 | 5.10 ± .2 | 3.12 ± .05 | 484 ± 2 | 137 ± 9 |
| --- | --- | --- | --- | --- |
| 3.56 ± .15 | x 6.20 ± .5 | x 1.15 ± .03 | (12.0 ± 1 | ( 1.78 ± .05 |
| 40.3 ± 3.5 |  |  |  |  |
| 77.0 ± 7.2 |  |  |  |  |

Word problems

| 21.2 ± 1.3 m/s | 0. A car goes 45 ± .5 m in 2.12 ± .11 seconds. What is the speed of the car, and what is the uncertainty of the speed? |
| --- | --- |
| 14.7 ± .8 m2 .77? | 1. What is the area (with uncertainty) in square meters of a rectangular room that measures 3.5 x 4.2 m where both measurements have an uncertainty of .1 m? |
| 140.4 ± 6.0 cm | 2. A staircase has 12 steps, each one being 11.7 ± .5 cm high. What is the total height of the staircase with uncertainty? (Add twelve together…) |
| 1.2 ± 1.3 cm Yes | 3. One board is 24.1 ± .5 cm long, and another is 25.3 ± .8 cm long. How much longer is the second than the first? Could the first possibly be longer? |
| 452.4 ± 7.5 cm2 | 4. What is the area (with uncertainty) of a circle that is 12.0 cm ± .1 cm in radius? (area = (r2 so that is (xrxr) |