PreQuiz 12.1

Standing Waves

Name

Foreign Language Name

Show your work, and circle your answers and use sig figs to receive full credit.

1-3. A guitar string has a length of 64.5 cm, and a fundamental frequency of 110. Hz.

1. Draw the first three harmonics of vibration on the string below, and calculate the wavelength and frequency  for each.

| . . | . . | . . |
| --- | --- | --- |
| 1.29 m, 110. Hz | .645 m, 220. Hz | .430 m, 330. Hz |

2. What is the velocity of the waves on this string? (142 m/s)

3. If this string is fingered 21.5 cm from one end (it is shortened by that amount).  What is the frequency of the fundamental now? (165 Hz)

4. Calculate the wavelengths below.  The length given is the length of the waveform (The picture)

L = 45 cm					L = 2.67 m				L = 68 cm

( = 36 cm						( = 2.67 m					( = 136 cm

5. Draw the second possible harmonic (The second lowest tone it can make.) of a one end fixed, one end open pipe.  Calculate the frequency of this mode if the pipe is 13.2 cm long, and the speed of sound in the pipe is 317 m/s. (1801 -> 1.80 x 103 Hz)