Digital Information Storage Objectives A-L

Objective A: Binary to decimal

Problems:

- Convert 10110110 to decimal. (182)

- Convert 11011011 to decimal. (219)

- Convert 00010111 to decimal. (23)

Objective B: Decimal to Binary

Problems:

- Convert 213 to an 8 bit binary. (11010101)

- Convert 117 to an 8 bit binary. (01110101)

- Convert 247 to an 8 bit binary. (11110111)

- Convert 129 to an 8 bit binary. (10000001)

Objective C-D: The advantages of digital information storage, and bit rate vs. sample depth.

Questions:

- What is the difference between a digital and an analog signal?

- How is analog converted to digital?

- What is meant by bit rate, and sample depth?

- What are the advantages of digital information storage?

Objective E-F: Storing information on CDs

Questions:

- How is digital information stored on a CD basically?

- What is the deal with constructive and destructive interference and the depth of pits?

Problems:

- What is the ideal pit depth for a 405 nm blu-ray laser? (101.25 ≈ 101 nm)

- An optical disc has a pit depth of 162.5 nm.  What is the best laser wavelength to read this? (650 nm)

- CDs use a 780 nm laser.  What is the ideal pit depth? (195 nm)

Objective G: Applying the Rayleigh Criterion to Optical Disc Readers

Questions:

- What is the idea behind the Rayleigh Criterion:

  - What is angle of resolution?

  - How does the wavelength of light used affect the angle of resolution?

  - How does the size of the aperture affect the angle of resolution?

Problems:

- An optical disc reader has a 3.2 mm diameter lens that is 2.0 mm from the disc.  What is the smallest pit separation it can resolve if it uses 405 nm light? (3.1E-7 m or .31 (m)

- You are designing an optical disc reader lens that must be 4.0 mm from a disc, and resolve pits that are 0.47 (m apart using 650 nm light.  What must be its diameter? (6.7 mm)

Objective H: Types of data storage

Questions:

- What basic types of digital storage are there?

- What are some main differences between RAM, and the hard disc on your computer?  What are the advantages of both?

Objective I: Basic Capacitance

Questions:

- What is a capacitor?

Problems:

- What is the capacitance if you can store 2.3 (C of charge at 12 V of potential? (1.9E-7 F)

- If you have 4.8 V across a 240 micro farad capacitor, what is the charge stored? (.0012 C)

- If you store 1.2 (C of charge on a 500. pF capacitor, what is the voltage? (2400 V)

- A 0.130 pF CCD pixel has a voltage of 1.70 mV across it.  How many electron charges does this represent? (1380 electron charges)

- If a 0.18 pF CCD pixel is hit by 1730 photons, what is the voltage across it if it has a quantum efficiency of 100%?  What if it is 70% efficient? (1.54 mV, 1.08 mV)

Objective J: CCD devices

Questions:

- If the pixels on a CCD device are like capacitors, how do they get charged?

- If CCD devices are black and white only, how are they used to create color images?

- Why is the “magnification” in a camera really smallification?  (i.e. a magnification smaller than one)

Objective K: Calculating Random Crap with CCD Devices

Problems:

- A camera has a 32.0 mm by 21.3 mm sensor that has 5380 x 3580 pixels.  It has a quantum efficiency of 72%.  Its pixels have a capacitance of 0.14 pF.

  - What is the area of a single pixel? (3.54E-11 m2)

  - If each pixel has 2.30 mV across it, how many electron charges is it holding? (2010 electron charges)

  - How many photons must have hit that area given the quantum efficiency? (2790 photons)

  - How many photons per square meter does this represent? (7.89E13 photons/m2)

  - If the camera used an exposure of 1/500 of a second, what is the light intensity in photons/s/m2? (3.94E16 photons/s/m2)

  - What is the “magnification” if an image of a 67 cm tall dog eating with a knife and fork forms an image that is 17 mm tall? (0.0254x)