Digital Information Storage  - Computers and digital electronics store data in binary form – either all “on” or all “off”

Binary to Decimal:

1101 =

Decimal to Binary:

| 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |
| --- | --- | --- | --- | --- | --- | --- | --- |

Convert  237 to binary:

Advantages of Binary:

Conversion of analog to digital:

Sample rate

Sample depth

Information storage on a CD (or DVD)

Destructive interference:

path difference = 1/2λ = 2d

d = depth of pit (m)

λ = laser wavelength (m)

Example – if the pits are 150 nm deep, what wavelength of laser light will create destructive interference relative to this depth?

Rayleigh Criterion and CD Laser Optics:

θ = Angle of resolution (Rad)

r = min distance separating pits (m)

d = distance to CD from lens (m)

λ = Wavelength of laser (m)

b = Diameter of CD Lens (m)

Example - DVDs have pits that are about 0.74μm apart.  If the lens has a diameter of 4.2 mm, and the laser has a wavelength of 780 nm, what must be the maximum distance from the lens to the disc so that the reader can resolve the pits?