## Slide 1
Formative Assessment

## Slide 2
1. A 600. kg stage set on frictionless air bearings goes from rest to 0.850 m/s in 12.5 seconds. What force acted on the set? (40.8 N)

## Slide 3
2. A 0.142 Kg baseball going 41.0 m/s, strikes a bat, and heads straight back to the outfield at 53.0 m/s. If the bat exerted a force of 2350 N, for what time was it in contact with the bat? (0.00568 s)

## Slide 4
3. A rocket engine burns 12.0 grams of fuel (0.0120 kg) in 1.10 seconds with an exhaust velocity of 782 m/s. What it the thrust of this engine? (8.53 N)

## Slide 5
4. A rocket engine burns fuel at a rate of 53.5 grams per second, and develops a force of 65.2 N. What must be the exhaust velocity? (1000 grams = 1 kg)
(1219 m/s)

## Slide 6
5. A 60.0 kg rocket, 48.0 kg of which is fuel, burns 2.15 kg of fuel per second with an exhaust velocity of 982 m/s. What are its initial and final acceleration as it takes off from earth? For what time do the engines burn? optional: (What is its acceleration at t = 10.0 s? Make a graph of the acceleration.)
(25.4 m/s/s, 166 m/s/s, 22.3 s, 45.0 m/s/s)

## Slide 7
more

## Slide 8
What force exerted for 0.12 seconds will make a 0.145 Kg baseball change its velocity 30. m/s toward the batter to 50. m/s toward the outfield? (97 N)

## Slide 9
A 310. kg rocket, 256 kg of which is fuel, burns all of its fuel in 37.0 seconds with an exhaust velocity of 881 m/s. What are its initial and final acceleration as it takes off from earth? (9.85 m/s/s, 103 m/s/s)

## Slide 10
A 16.0 kg rocket, 12.0 kg of which is fuel, burns its fuel at a rate of 0.382 kg/s with an exhaust velocity of 642 m/s. What are its initial and final acceleration as it takes off from earth? (5.52 m/s/s, 51.5 m/s/s)

## Slide 11
question