## Slide 1
Angular Mechanics - Kinematics
Contents:
  Radians, Angles and Circles
  Linear and angular Qtys
  Conversions | Whiteboard
  Tangential Relationships
    Example | Whiteboard
  Angular Kinematics
    Example | Whiteboard

## Slide 2
Angular Mechanics - Radians
r

s
Full circle:
  360o = 2 Radians
 = s/r
Radians = m/m = ?

## Slide 3
Conversions
Radians
Revolutions
Rad/s
Rad/s
RPM (Rev/min)
= rev x (2)
= rad  (2)
= RPM x (2)  (60)
= (rev/s) x (2)
= (rad/s) x (60)  (2)

## Slide 4
Whiteboards:
Conversions
1 | 2 | 3 | 4

## Slide 5
How many radians in 3.16 revolutions?
rad = rev(2)
rad = (3.16 rev)(2) = 19.9 rad
19.9 rad

## Slide 6
If a drill goes through 174 radians, how many revolutions does it go through?
rev = rad/(2)
rev = (174 rad)/(2) = 27.7 rev
27.7 rev

## Slide 7
Convert 33 RPM to rad/s
rad/s = (rev/min)(2 rad/rev)(min/60s)
= (33rev/min)(2 rad/rev)(min/60s)
rad/s = 3.5 rad/s
3.5 rad/s

## Slide 8
Convert 12 rev/s to rad/s
rad/s = (rev/s)(2 rad/rev)
rad/s = (12 rev/s)(2 rad/rev)
rad/s = 75 rad/s
75 rad/s

## Slide 9
Convert 45.0 rad/s to RPM
rad/s = (rev/s)(2 rad/rev)
rad/s = (12 rev/s)(2 rad/rev)
rad/s = 75 rad/s
430. RPM

## Slide 10
Convert 23.0 rad/s to rot/s
rad/s = (rev/s)(2 rad/rev)
rad/s = (12 rev/s)(2 rad/rev)
rad/s = 75 rad/s
3.66 rot/s

## Slide 11
Angular Mechanics - Tangential Relationships
Linear:
(m) s
(m/s) v
(m/s/s) a
Tangential: (at the edge of the wheel)
= r - Displacement*
= r - Velocity
= r - Acceleration*
*Not in data packet

## Slide 12
Example: s = r, v = r, a = r
A certain gyro spinner has an angular velocity of 10,000 RPM, and a diameter of 1.1 cm. What is the tangential velocity at its edge?
v = 5.8 m/s

## Slide 13
Whiteboards:
Tangential relationships
1 | 2 | 3 | 4 | 5 | 6

## Slide 14
What is the tangential velocity of a 13 cm diameter grinding wheel spinning at 135 rad/s?
8.8 m/s

## Slide 15
What is the angular velocity of a 57 cm diameter car tire rolling at 27 m/s?
95 rad/s

## Slide 16
A 0.450 m radius marking wheel rolls a distance of 123.2 m. What angle does the wheel rotate through?
274 rad

## Slide 17
A car with 0.36 m radius tires speeds up from 0 to 27 m/s in 9.0 seconds.
(a) What is the linear acceleration?
3.0 m/s/s

## Slide 18
A car with 0.36 m radius tires speeds up from 0 to 27 m/s in 9.0 seconds.
(a) a = 3.0 m/s/s
(b) What is the tire’s angular acceleration?
8.3 Rad/s/s

## Slide 19
A car with 0.36 m radius tires speeds up from 0 to 27 m/s in 9.0 seconds.
(a) a = 3.0 m/s/s
(b)  = 8.3 Rad/s/s (8.33333333)
(c) What angle do the tires go through?
340 Rad

## Slide 20
Angular Mechanics - Angular Quantities
Linear:
(m) s
(m/s) u
(m/s) v
(m/s/s) a
(s) t
Angular:
 - Angle (Radians)
i - Initial angular velocity (Rad/s)
 f - Final angular velocity (Rad/s)
 - Angular acceleration (Rad/s/s)
t - Uh, time (s)

## Slide 21
Angular Kinematics
Linear:
u + at = v
ut + 1/2at2 = s
u2 + 2as = v2
(u + v)t/2 = s
Angular:
f = i + t
 = it + 1/2t2
f 2 = i2 + 2
 = (i + f)t/2*
*Not in data packet

## Slide 22
Example: My gyro spinner speeds up to 10,000 RPM, in 0.78 sec.
What is its angular acceleration?
What angle does it go through?
What distance does a point on the edge travel if the diameter is 1.1 cm?
1342.6=1300 rad/s/s
408.4 = 410 rad
s = 2.25 m

## Slide 23
Whiteboards:
Angular Kinematics
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8

## Slide 24
A turbine speeds up from 34 rad/s to 89 rad/s in 2.5 seconds. What is the angular acceleration?
22 rad/s/s

## Slide 25
A drill slows from 145 rad/s to 54.0 rad/s with an angular acceleration of -1.80 rad/s/s. Through what angle did it go?
How many rotations?
5030 radians, 801 rotations

## Slide 26
A motor going 45.0 rad/s has an angular acceleration of 12.4 rad/s/s for 3.70 seconds. What angle does it go through?
251 rad

## Slide 27
A hard drive speeds up from rest to 4200. RPM in 3.50 seconds. How many rotations does it make doing this?
122.5 rotations

## Slide 28
A potter’s wheel is spinning at 71.0 RPM and stops in 5.30 revolutions. (a) What is its angular deceleration in rad/s/s?
-0.830 rad/s/s

## Slide 29
A hard drive slows from 7200. RPM to rest in 16.2 seconds. What distance does a point 3.10 cm from the center travel as it is slowing down?
189 m

## Slide 30
A car with 0.68 m diameter tires has an acceleration of 3.60 m/s/s. Through what angle do the tires go when the car speeds up from 12.0 m/s to 32.0 m/s? How many rotations?
359 radians, 57.2 rotations

## Slide 31
A drill speeds up from 16.0 rot/sec to 72.0 rot/sec in 10.0 sec. How many rotations does it go through?
440 rotations