## Slide 1
Formative Assessment

## Slide 2
1. A bicycle going 13.5 m/s has 0.680 cm diameter wheels. What is the angular velocity of the wheels in rad/s? in RPM? (39.7 rad/sec, 379 RPM)

## Slide 3
2. What is the tangential velocity of a 4.50 cm radius hard drive spinning at 5200. RPM? (24.5 m/s)

## Slide 4
3. What time will it take a wheel to speed up from 12.0 rad/s to 47.0 rad/s with an acceleration of 1.40 rad/s/s? (25.0 s)

## Slide 5
4. A hard drive takes 4.80 s to speed up from rest to 7200. RPM. How many revolutions does it go through in doing this? (288 revolutions)

## Slide 6
5. A car with 0.450 m radius wheels speeds up to 28.0 m/s over a distance of 112 m with an acceleration of 2.60 m/s/s. What is the initial angular velocity of the wheels? (31.6 rad/s)

## Slide 7
practice problems

## Slide 8
1. A 0.0760 m diameter (76 mm) skateboard wheel rolls through 137 rotations. What linear distance did it travel? (32.7 m)
s = θr
v = r
a = r

## Slide 9
2. What is the angular acceleration of a 0.630 m diameter bicycle wheel if it is accelerating linearly at 8.20 m/s/s? (26.0 rad/s/s)
s = θr
v = r
a = r

## Slide 10
3. A 0.0660 m diameter skateboard wheel travels 12.0 m. How many rotations does it go through? (57.9 rotations)
s = θr
v = r
a = r

## Slide 11
4. A 0.650 m diameter wheel accelerates at 1.54 rad/s/s. What is the tangential acceleration of the edge? (0.5005 m/s/s)
s = θr
v = r
a = r

## Slide 12
5. A wheel goes through 143 rotations when it rolls linearly 14.2 m. What is the radius of the wheel? (0.0158 m)
s = θr
v = r
a = r

## Slide 14
6. What is the linear velocity 0.120 m from the center of a grinding disk spinning at 1450 RPM? (18.2 m/s)
s = θr
v = r
a = r

## Slide 15
7. What is the angular velocity of a 0.920 m radius aircraft tire in rotations/second when it is has a linear velocity of 48.0 m/s?
(8.30 rot/s)
s = θr
v = r
a = r

## Slide 16
8. A merry go round spins at 0.590 rotations/second. What is the tangential velocity 1.80 m from the center? (6.67 m/s)
s = θr
v = r
a = r

## Slide 17
9. A 0.940 m diameter wheel has a tangential velocity at its edge of 25.0 m/s. What is its angular velocity in RPM? (508 RPM)
s = θr
v = r
a = r

## Slide 18
10. A hard drive spins at 7200 RPM. What distance from the center has a tangential velocity of 12.0 m/s? (0.0159 m)
s = θr
v = r
a = r

## Slide 20
11. A drill going 98.0 rad/s decelerates at -1.20 rad/s/s for 15.0 s. What is the final angular velocity in rad/s? (80.0 rad/s)
θ
i
f

t

## Slide 21
12. A drill speeds up from rest to 156 rad/s in 5.70 s. Through what angle in radians does it go? (445 rad)
θ
i
f

t

## Slide 22
13. A drill goes through 132 radians in 8.80 s slowing to rest. What was its initial angular velocity in rad/s? (30.0 rad/s)
θ
i
f

t

## Slide 23
14. A drill speeds up from 11.0 rad/s to 35.0 rad/s in 184 radians. What is its angular acceleration? (3.00 rad/s/s)
θ
i
f

t

## Slide 24
15. A drill goes through 526 radians accelerating at 2.58 rad/s/s from rest. What is its final angular velocity in rad/s? (52.1 rad/s)
θ
i
f

t

## Slide 26
16. A motor speeds up from 1350. RPM with an angular acceleration of 2.90 rad/s/s for 19.0 seconds. Through what angle in radians does it rotate? (3210 rad)
θ
i
f

t

## Slide 27
17. A car tire initially rotating at 37.0 rotations per second slows down through 148 rotations in 5.20 seconds. What is its final angular velocity in rotations per second? (19.9 rot/s)
θ
i
f

t

## Slide 28
18. A drill speeds up from 680. RPM to 1540 RPM with an acceleration of 1.80 rad/s/s. How many rotations does it go through? (926 rotations)
θ
i
f

t

## Slide 29
19. A skateboard wheel speeds up from 5.30 rotations/sec to 12.0 rotations/s in 9.00 seconds. What is the angular acceleration in rad/s/s? (4.68 rad/s/s)
θ
i
f

t

## Slide 30
20. A turntable accelerates at 0.835 rad/s/s from rest to 33.3 RPM. What is its angular displacement in radians? (7.28 rad)
θ
i
f

t

## Slide 32
21. A car with 0.340 m radius tires going 19.2 m/s decelerates at 1.20 m/s/s for 2.30 s. What is the final angular velocity of the tires?
(48.4 rad/s)
θ
i
f

t

## Slide 33
22. A car with 0.840 m diameter wheels accelerates from rest with an acceleration of 6.40 m/s/s for 3.50 seconds. Through what angle in radians do the wheels go? (93.3 radians)
θ
i
f

t

## Slide 34
23. A 0.110 m radius ball going 5.80 m/s rolls to a stop in 9.70 seconds. What was the angular acceleration of the ball in rad/s/s?
(-5.44 rad/s/s)
θ
i
f

t

## Slide 35
24. A 0.360 m radius car tire goes from 12.5 rad/s to 36.8 rad/s with a linear acceleration of 3.90 m/s/s. What linear distance does the car travel? (19.9 m)
θ
i
f

t

## Slide 36
25. A 0.125 m radius grinding wheel speeds up from 142 rad/s to 259 rad/s in 13.0 s. Through what distance does a point in the edge of the wheel travel in this time? (326 m)
θ
i
f

t