## Slide 1
Formative Assessment

## Slide 2
1. Find the forces F1 and F2 (magnitude and direction). Assume the beam is uniform. (-66.2 N (down), 361 N (up))
18.0 kg
12.0 kg
F2
F1
5.5 m
9.00 m
4.00 m

## Slide 3
1a 1. The beam is 6.10 m long, and the person is standing 1.10 m from the right side. Find the tensions in the cables.
(T1 = 402 N up, T2 = 854 N up)
56.0 kg
72.0 kg
T1
T2

## Slide 4
1b 3. The beam is 8.20 m long, and F2 is 3.00 m from the left side, and the person is 0.500 m from the right side. Find the forces exerted by the supports.(F1 = 1030 N down, F2 = 1830 N up)
18.0 kg
63.0 kg
F1
F2

## Slide 5
2. Find the tension in the cable, and the components of the force that the wall exerts: Wx and Wy. Show all three equations of equilibrium: x, y and torque. The sign has a mass of 14.0 kg and hangs 3.10 m from the left side. The cable forms an angle of 32.0o with the beam and is connected 0.900 m from the right end. The uniform beam is 5.00 m long, and has a mass of 21.0 kg. (T = 433 N, Wx = +367 N right, Wy = +114 N up)
Bob’s Fish and Bait

## Slide 6
2a 1. The cable is connected 6.00 m from the left side of, and makes an angle of 39.0o with the 10.0 m long beam. Find the tension in the cable, and the horizontal and vertical components of the force exerted by the wall. Be sure to give the direction of the components.
(T = 351 N, Wx = 273 N right, Wy = 34.3 N down)
11.0 kg
8.00 kg

## Slide 7
2b 3. The horizontal cable is connected 4.70 m from the hinge, and makes an angle of 54.0o with the 5.00 m long, 5.30 kg beam. The sign hangs 3.00 m from the hinge. Find the tension in the cable, and the horizontal and vertical components of the force exerted by the wall. Be sure to give the direction of the components. (T = 38.3 N, Wx = 38.3 N right, Wy = 91.2 N up)
4.00 kg

## Slide 8
2c 6. The rod is connected 3.20 m from the left side of, and makes an angle of 38.0o with the 4.00 m long beam. The box is centered 1.20 m from the left side. Find the force along the rod, and the horizontal and vertical components of the force exerted by the wall. Be sure to give the direction of the components. (F = 57.8 N, Wx = 45.5 N left, Wy = 33.1 N up)
4.00 kg
3.00 kg

## Slide 9
question