## Slide 1
Formative Assessment

## Slide 2
1a. Convert 1340. Torr absolute to gauge pressure psi. (11.2 psi gauge )
1.00 atm = 1.013x105 Pa = 101.3 kPa = 760. Torr = 14.7 psi

## Slide 3
1b. Convert 87.3 kpa gauge to Torr absolute (1415 Torr absolute)
1.00 atm = 1.013x105 Pa = 101.3 kPa = 760. Torr = 14.7 psi

## Slide 4
2. A cannon ball has a density of 7820 kgm-3 and a mass of 23.2 kg. What is its radius if it is perfectly spherical?
(8.91 cm)

## Slide 5
3. A hydraulic jack has an input piston diameter of 0.850 cm, and an output piston diameter of 4.50 cm. What force must you exert on the input piston to lift a 1210 kg car? (424 N )

## Slide 6
4. At what depth in mercury (ρ = 13.6x103 kg m-3) is the absolute pressure 482 kPa? (Assume the pressure above the mercury is 1 atm) (2.85 m )

## Slide 7
5. A cylinder has a radius of 0.920 cm and is 25.0 cm long. How far will it sink into a mixture with a density of 865 kg m-3 if it has a mass of 37.5 grams assuming it is weighted so it floats vertically? (16.3 cm )

## Slide 8
Practice

## Slide 9
UC1 What is 12.0 psi gauge in Pa absolute? (1.84E5 Pa)

## Slide 10
UC2 What is 34,500 Pa absolute in atm gauge? (-0.659 atm)

## Slide 11
6. A sphere that contained 45.0 kg of air would have what radius? (ρ = 1.29 kgm-3) (2.03 m)

## Slide 12
8. What is the mass of mercury (ρ = 13.6x103 kgm-3) in a (cylindrical) cup that is 9.00 cm tall, and 11.0 cm in diameter? (11.6 kg)

## Slide 13
10. A hydraulic jack lifts 620. kg of mass with an input force of 24.0 N. What is the diameter of the input cylinder if the output cylinder has a diameter of 12.6 cm? (0.791 cm)

## Slide 14
12. A brake cylinder exerts 342 N of force with an input force of 55.2 N. What is the diameter of the brake cylinder if the master cylinder has a diameter of 1.21 cm? (3.01 cm)

## Slide 15
17. At what depth below the ocean (ρ = 1025 kgm-3) is the absolute pressure 100. psi? (Assume the pressure above the surface is 1 atm) (58.5 m)

## Slide 16
19. There is a gauge pressure of 812 Torr at a depth of 14.2 m in a fluid. What is the density of the fluid? Assume there is 1 atm above the fluid. (777 kgm-3)

## Slide 17
20. At what depth in the dead sea (ρ = 1240 kgm-3) does the water exert a force of 23,500 N on a 9.20 cm diameter porthole? Assume there is 1 atm above the water. (282 m)

## Slide 18
21. A tank contains Liquid nitrogen (ρ = 808 kgm-3). At a depth of 13.5 m there is an absolute pressure of 313.7 kPa. What is the pressure at the top of the liquid in psi? (30.0 psi)

## Slide 19
25. What downward force would you need to exert to keep a 14.0 cm radius sphere with a density of 253 kgm-3 submerged in a fluid with a density of 965 kgm-3? (80.3 N)

## Slide 20
26. What upward force would you need to exert on a 52.1 kg piece of basalt (2920 kgm-3) submerged in the dead sea where the water has a density of 1240 kgm-3 to keep it from sinking? (294 N)

## Slide 21
27. A 13.25 gram hydrometer is a 1.12 cm diameter tube weighted on one end so it floats upright in a liquid. If it is 25.0 cm long, but floats with 7.80 cm exposed to air, what is the density of the liquid? (782 kgm-3)

## Slide 22
28. A hot air balloon is 8.74 m in radius (assume it is spherical) and contains hot air with a mean density of 0.9486 kgm-3. Calculate the lifting capacity of the hot air if it is surrounded by air with a density of 1.34 kgm-3. (10,740 N)

## Slide 23
29. A glass (2580 kgm-3) cylindrical stirring rod is 5.02 mm in diameter and 18.0 cm long. What force do I need to exert on it to hold it vertically at rest with the tip submerged in acetone (791 kgm-3) to a depth of 11.0 cm? (7.33x10-2 N)

## Slide 24
30. A rectangular piece of wood that measures 13.0 cm x 15.2 cm x 3.78 cm floats face down in a fluid with a density of 893 kgm-3 with 2.93 cm of the 3.78 cm dimension submerged. What is the density of the wood? (692 kgm-3)

## Slide 25
31. A 5.34 kg piece of rock can be supported by a force of 40.4 N when submerged in water with a density of 1008 kgm-3. What is the density of the rock? (4406 kgm-3)

## Slide 26
32. A 1.28 kg piece of Styrofoam float material can be held under water (ρ = 1000. kgm-3) with a downward force of 328.7 N. What is the density of the Styrofoam? (36.8 kgm-3)