## Slide 1
Voltage and Electric Field
Contents:
    Voltage, work and charge
      Voltage example
      Whiteboards
    Voltage and electric field
      Example
      Whiteboards
    Electron Volts and accelerated ions

## Slide 2
Electrical Potential (AKA Voltage)
Definition:
  V = W
  q
        V = Change in Electrical potential (Volts)
        W = Work (J)
        q = Charge (C)
Voltage is like pressure, Air = 10,000 V/in, Show, Pickle-luminescence, Zap-O-Rama

## Slide 3
Hans Full does 0.012 J of work on 630 C of charge moving it against an electrical field. What is the change in voltage?
Jerry Rigg moves a 2.0 kg object upwards doing 64 J of work. What is the change in gravitational potential?
(32 J/kg)
(19 J/C or 19 V) – show units

## Slide 4
Whiteboards:
Potential, Work and Charge/Mass
1-5

## Slide 5
10.0 V
V = Ep/q, Ep = 125 J, q = 12.5 C
V = 10.0 V
Sandy Deck does 125 J of work on a 12.5 C charge. Through what voltage did she move it?

## Slide 6
0.600 J
Lila Karug moves a 120. C charge through a voltage of 5000. V. How much work does she do?
V = Ep/q, q = 120x10-6 C, V = 5000. V
Ep = 0.600 J

## Slide 7
9.0 J/kg
Benny Hana does 45.0 J of work on 5.0 kg of mass moving it against a gravitational field. What is its change of gravitational potential?
solution

## Slide 8
0.050 kg or 50. grams
Jane Linkfence moves a mass through a potential difference of 320 J/kg and does 16 J of work. What is the mass?
solution

## Slide 9
13.8 mC
Arthur Moore does 0.167 J of work moving an unknown charge through a voltage of 12.1 V. Please, please, won’t you please help him calculate the charge?
V = Ep/q, V = 12.1 V, Ep = 0.167 J
q = 0.013801653 = .0138 C = 13.8 mC

## Slide 10
Voltage and distance and E Field
Definition: (derive)
  E = -ΔV
  Δr
  E = Electric Field
  ΔV = Voltage change
  Δr = displacement over which it changes
  (Why the minus sign)
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Parallel Plates
Δr
E

## Slide 11
What is the electric field when you have 12.0 V across two || plates that are separated by 0.0150 m?
If you have a gravitational field strength of 9.81 N/kg, what is the change of gravitational potential in a vertical upward distance of 1.85 m?
(18.1 J/kg)
(800 V/m) – show units = N/C

## Slide 12
Whiteboards:
Potential, Field, and distance
1-5

## Slide 13
5.0x102 V/m right
Lee DerHosen places a voltage of 25 V across two || plates separated by 5.0 cm of distance. What is the electric field generated? Which way is the field?
+
+
+
+
+
+
+
+
+
+
-
-
-
-
-
-
-
-
-
-
Parallel Plates
5cm
+25 V
0 V

## Slide 14
0.39 V, right side is +
Art Zenkraftz measures a 125 V/m electric field to the left between some || plates separated by 3.1 mm. What must be the voltage across them? Which
side is the positive?
Parallel Plates
3.1 mm
E

## Slide 15
14.5 m
Helen A. Handbasket lifts a mass upwards (on earth) increasing its gravitational potential by 142 J/kg. What vertical distance did she lift it?

## Slide 16
An electric field exerts a Southerly force of 3.30 N on a +450. µC charge. What is the change in potential if you displace yourself 7.30 m to the North? Is it an increase, or decrease in potential?
+53,500 V, increase

## Slide 17
A gravitational field exerts a force of 126. N on a 13.0 kg mass away from point B and toward point A that is vertically displaced from B a distance of 12.0 m. What is the field strength? In what direction? What is the change in gravitational potential if you go from B to A?
9.69 N/kg, toward A, -116 J/kg

## Slide 18
A uniform electrical field changes electrical potential from 110. V to 370. V when you move down 6.10 m. What is the magnitude and direction of the electrical field, and what force does it exert on a -1.40 µC charge?
42.6 V/m. up, 5.97x10-5 N down

## Slide 19
If you move a mass vertically from point A to point B, the potential changes from -65.0 J/kg to -34.0 J/kg in a distance of 17.0 m. What is the gravitational field strength? Does the field point toward A or B? Which point is at a higher elevation, A or B?
1.82 N/kg toward A, B is higher.

## Slide 21
43 V, bottom
E = -ΔV/Δx, F = Eq, F = mg
mg = Eq = ΔVq/Δx
V = 42.875 V = 43 V
Bottom positive
Carson Busses needs to suspend a 1.5 g (.0015 kg) pith ball against gravity. (gravity = electric) It has a charge of +12 C, and he is generating the electric field using plates that are 3.5 cm apart. What voltage should he use? Which side (top or bottom) is positive?
+Q

## Slide 22
7.92 N/kg
Mimi O’ Graf is on planet Xzrstlnr. If she increases the gravitational potential of a mass by 95.0 J/kg in a vertical distance of 12.0 m, what is the gravitational field strength?
sol

## Slide 23
12 cm
Oliver Goodguy needs to generate a 13 V/m electric field using a 1.50 V source. What distance should he separate || plates to generate this electric field?
E = -ΔV/Δx, ΔV = 1.50 V,, E = 13 V/m
Δx = 0.1154 m = 0.12 m = 12 cm