## Slide 1
Formative Assessment

## Slide 2
question

## Slide 3
practice problems

## Slide 5
1. a. A loop or wire with a radius of 0.430 m starts at an angle of 75.0o with the page, and is rotated to the plane of the page. If there is a 6.95 T magnetic field into the page, and the rotation takes .00500 s, what is the average EMF generated? Which way does it flow? (598 V, acw)

## Slide 6
b. A vertical wire in the plane of the page traveling to the right is moving at 1.05 m/s through a 7.24 T magnetic field out of the page. What is its length if there exists a potential of 4.72 V from one end to the other? Which end is positive, the top or the bottom? (0.621 m, bottom)

## Slide 7
c. A transformer has 3800. primary windings, and 550. secondary windings. What is the voltage in the primary if there is a voltage of 72.6 V (AC) in the secondary? (502 V)

## Slide 8
d. You want to step 120. VAC down to 6.12 VAC with a transformer. What should be the number of secondary windings if you have 540. primary windings? (27.5 windings)

## Slide 9
e. A transformer has 0.258 A flowing in the primary side, and 12.7 A flowing in the secondary. What is the voltage on the primary side if the secondary side is at 2.27 VAC? (112 V)

## Slide 11
2. a. A loop or wire with a radius of 0.900 m is in the plane of this page, and is rotated so that the loop forms a 42.0o angle with the page. If there is a 5.73 T magnetic field into the page, and this generates an EMF of 16.7 V, in what time did the loop undergo the rotation, and which way did the current flow? (CW or ACW) (0.224 s, cw)

## Slide 12
b. A vertical wire in the plane of the page is 2.86 m long, and is traveling to the left at 16.0 m/s through a magnetic field perpendicular to the page. There exists a potential of 19.2 V between one end and the other. The top is positive. What is the magnitude of the magnetic field, and is it into or out of the page? (0.420 T out of page)

## Slide 13
c. A transformer has 9800. primary windings, and 710. secondary windings. What is the voltage in the secondary if there is a voltage of 303 V (AC) in the primary? (22.0 V)

## Slide 14
d. You want to step 120. VAC down to 24.0 VAC with a transformer. What should be the number of primary windings if you have 1300. secondary windings? (6500 windings)

## Slide 15
e. A transformer has 5.87 A flowing in the primary side, and 1.15 A flowing in the secondary. What is the voltage on the secondary side if the primary side is at 110. VAC? (561 V)

## Slide 17
question

## Slide 18
question